Table 1 Principal Particulars of Ship A-2

| Items | Ship | 1/15scaled model |
| --- | --- | --- |
| length : Lpp | 34.5 m | 2.3 m |
| breadth : B | 7.60 m | 0.507 m |
| depth : D | 3.07 m | 0.205 m |
| draught at FP : Tf | 2.50 m | 0.166 m |
| mean draught : T | 2.65 m | 0.176 m |
| draught at AP : Ta | 2.80 m | 0.186 m |
| block coefficient : Cb | 0.597 | 0.597 |
| prismatic coefficient : Cp | 0.769 | 0.769 |
| water plane coefficient : Cw | 0.985 | 0.985 |
| wetted surface area : SF | 324 m2 | 1.44 m2 |
| projected lateral area of the portion of the ship and deck cargo above water line: A vertical distance from the centre of the projected vertical area of the ship above the water line, to the water line: h roll radius of gyration : xx/Lpp | 142 m2 2.63 m N/A* | N/A* N/A* N/A* |
| pitch radius of gyration : yy/Lpp | 0.302 | 0.302 |
| yaw radius of gyration : zz/Lpp | 0.302 | 0.302 |
| longitudinal position of centre of gravity from the midship : xCG | 1.31 m aft | 0.087 m aft |
| vertical position of centre of gravity from the keel line : KG | 3.36 m | 0.224 m |
| metacentric height : GM | 1.00 m | 0.0667 m |
| natural roll period : T | 7.4 s | 1.9 s |
| rudder area : AR | 3.49 m2 | 0.0155 m2 |
| rudder aspect ratio :  | 1.84 | 1.84 |
| vertical location of top of the rudder from the keel line | 1.52 m | 0.101 m |
| vertical location of bottom of the rudder from the keel line down flooding point : longitudinal position from AP : transverse position from centre line : vertical position from keel line | -1.05 m 29.3 m 2 m 3.199 m | -0.07 m N/A* N/A* N/A* |
| propeller diameter : DP | 2.60 m | 0.173 m |
| propeller pitch ratio : P/DP | 0.5778 | 0.5778 |
| bilge keel area | 5.10 m2 X 2 | 0.0227 m2 X 2 |
| position of fore end of bilge keel from the midship | 6.22 m fore | 0.415 m fore |
| position of aft end of bilge keel from the midship | 8.60 m aft | 0.573 m aft |
| breadth of bilge keel | 0.35m | 0.023 m |
| maximum limit of rudder angle | 35degrees | 35 degrees |
| maximum limit of rudder angular velocity | 7.5 degrees/s | 29 degrees/s |
| time constant of steering gear : TE | 0.63 s | 0.16 s |

* The virtual roll radius of gyration, Ixx+Jxx , can be estimated with the metacentric height and natural roll period as follows:  where  and g are the water density and gravity acceleration, respectively.